## Slide 1
F2B Judging Recommendations
This is no FAI/CIAM rule
Notes: Proper F2B judging requires considerable effort to acquire the knowledge and maintain the operational capability of the judges.
A corresponding commitment is the indispensable basic requirement in order to be able to provide an appropriate level of knowledge and ability of the judges to the competitors at the competition who practice in a disciplined manner and often travel from far away.
The scores given by individual judges to the same manoeuvre of a pilot may differ considerably.
Such differences are not so much due to training and experience, but to an individually different weighting of detected errors.
Recommendations for the interpretation of the FAI regulations and their uniform implementation at national levels are sustainable and effective contributions to an internationally comparable perception of errors and their weighting in scoring.

## Slide 2
Recommendations for judges F2B
Rules
Manoeuvres and Critical Points
Judging
Typical Errors
Error Weighting and Scoring
Fachkommission Fesselflug F2 Schweizerischer Modellflugverband SMV
These recommendations do not constitute FAI/CIAM regulations. The purpose of the presentation is to provide national model aviation organisations with guidance on the uniform training of judges for the evaluation of F2B flights.

## Slide 3
SPORTING CODE-SECTION 4 AEROMODELLING
Basics for all classes, organisation: CIAM General Rules 21. pdf
All classes F2: CIAM F2 controlline 21 .pdf
Manoeuvre diagrams F2B: CIAM F2 controlline annex 4 j 21 .pdf
The original text in English is binding
1. Rules
The FAI / CIAM rules for the F2B class are regularly adapted to the state of the art. The CIAM F2 Control-Line Subcommittee is responsible for the content:
https://www.fai.org/page/f2-control-line
Current rules: https://www.fai.org/page/ciam-code
Notes: This presentation is based on the FAI Sporting Code 2021.

## Slide 4
Changes to the rules
Anyone is entitled to request changes to the rules. Proposals are to be submitted to the FAI / CIAM through a national model flying organisation
https://www.fai.org/ciam-documents
- CIAM FORMS & OTHER DOCUMENTS
- CIAM Proposal Forms and Guidelines
- CIAM Proposal Form for Sporting Code Section 4
The Plenary Assembly of the national CIAM delegates decides on the changes.

## Slide 5: 2. Manoeuvres and Critical Points
Class F2B - CL Aerobatics and Annex 4 j – Class F2B Manoeuver Diagrams
Notes: This presentation is limited to the transfer of basic knowledge. It contains supplementary recommendations on how to apply to the FAI / CIAM rules.

## Slide 6
All text and diagrams for the manoeuvres describe the figures as the pilot sees them from the centre of the circle.
Notes: The F2B regulations are binding rules for the pilots. They define the prescribed flight path of the model on the "flight plane".
For the pilot, his model is always in the centre of his field of view. Because the aircraft is always at the same distance from him, the pilot perceives his manoeuvres as if they were executed on a "plane".
The drawings in Annex 4 j show the manoeuvres as the pilot sees them on the inner surface of his flying hemisphere.
The judge standing outside the hemisphere perceives the flown manoeuvres differently. As a result of the changing distance of the aircraft, from his point of view the manoeuvres appear as three-dimensional objects. These are also distorted differently, depending on the observer's location.
Which means that a number of judges standing at a distance next to each other see the same manoeuvre differently. This perception of the judge cannot be easily represented graphically, because the degree of distortion depends not only on the location of the judge, but also on his exact viewing direction. 3-D images created by common methods, as well as video recordings, can only approximate the individual perception of the F2B judge, but not exactly.
Regardless of this, the judge must learn to recognize a figure flown exactly according to the rules as such.

## Slide 7
4.2.15.1 Terminology and Wording
Flight Hemisphere: The hemisphere on which the model moves.
Base: The lower edge of the hemisphere. It is located at a height of 1.5 m above the highest point of the center of the circle.
Parallel: (Minor Circle ) An imaginary line on the surface of the hemisphere. It results when the model is flown with a constant line angle.
Great Circle: A straight line (as seen from the pilot) flown on the surface of the hemisphere. Examples: Horizontal- inverted flight, wingover and the horizontal connecting lines in the cloverleaf.
Horizontal: Flight on the base (great circle) or parallel to base (minor circle)
Vertical: A climb or dive flown at right angles to the base.
90° Wingover Path: A straight path (great circle) 90° to the base, passing over the highest point of the hemisphere.

## Slide 8
4.J.1. Take-off (Rule 4.2.15.3)
The takeoff run measures at least 4.5 m or maximum 1/4 - lap.
The distance from Start to reaching the level of horizontal flight measures one lap
Two laps of horizontal flight at the height of the base (+/- 30 cm) are part of the manoeuvre.
Notes: Too short or too long a take-off run is a fault.
Uneven climb is a fault.
An altitude of more than 1.8 m, or less than 1.2, m during the two laps of level flight is a fault.
Visible corrections of altitude during the first two laps of level flight are faults.

## Slide 9
4.J.2. Reverse wingover (Rule 4.2.15.4)
All turns tight.
Turns flown wide are errors.
Vertical through the top point of the hemisphere
Horizontal along the base
Turns exactly 180° opposite
Notes: The 2021 edition of the rules abandons the specification in meters for the radius of the corners in all cornered manoeuvres. The definition of the turns in the Rules is replaced by the terms: Smooth, precise and being of a tight radius.
This new definition is supplemented with the clarification in 4.B.7 b. of the Class F2B Judge's Guide: (excerpt)
The model shall turn as sharp (tight) as possible.
The highest scoring marks shall be assigned to the tightest corners.

## Slide 10
Three consecutive inside loops (Rule 4.2.15.5)
Circular shape
Line elevation angle at the highest point 45°
The second and third loops should be placed in exactly the same position as the first loop, and should be of exactly the same size

## Slide 11
Two consecutive laps of inverted level flight (Rule 4.2.15.6)
At the beginning of round 3, the entry altitude at the start is: base plus/minus 30 cm (1.2 - 1.8m.
The altitude must be maintained in laps 3 and 4 without visible correction.
Notes: Laps 1 and 2 are the recommended entry procedure
Laps 3 and 4 are judged
An altitude of more than 1.8 m, or less than 1.2, m during the two laps of inverted flight is an error.
Visible corrections of altitude during the two laps of inverted flight are faults.
Laps 5 and 6 are the recommended exit procedure

## Slide 12
Three consecutive outside loops (Rule 4.2.15.7)
Circular shape
Line elevation angle at the highest point 45°
The second and third loops should be placed in exactly the same position as the first loop, and should be of exactly the same size

## Slide 13
Two consecutive inside square loops (Rule 4.2.15.8)
All turns tight. Turns flown wide are defects.
Along the base, the width, including both turns, is 1/8 lap.
From the pilot's point of view, verticals (90°) are flown perpendicular to the base.
The upper side is flown with 45° line elevation angle. It is, at the 45° elevation, 1/8 lap wide, but shorter in meters length than the width at the base.
Both in the same place.

## Slide 14
Two consecutive outside square loops (Rule 4.2.15.9)
All turns tight. Turns flown wide are defects.
Along the base, the width, including both turns, is 1/8 lap.
From the pilot's point of view, verticals (90°) are flown perpendicular to the base.
The upper side is flown with 45° line elevation angle. It is, at the 45° elevation, 1/8 lap wide, but shorter in meters length than the width at the base.
Both in the same place.

## Slide 15
Two consecutive inside triangular loops (Rule 4.2.15.10)
All turns tight. Turns flown wide are defects.
Along the base, the width, including both turns, is slightly more than 1/8 lap (+).
The top corner reaches a maximum of 45° line elevation angle.
Both in the same place

## Slide 16
Two consecutive horizontal eight (Rule 4.2.15.11)
The highest point of both loops reaches a maximum line elevation angle of 45°
The loops have a circular round shape and touch each other tangentially
When flying through the intersection the model flies momentarily vertical
All crossings are in the same place

## Slide 17
Two consecutive horizontal square eight (Rule 4.2.15.12)
All turns tight. Turns flown wide are faults.
Along the base, the width of each loop, including both turns, is 1/8 of a lap.
The upper sides are flown at 45° line angle. They are, at the 45° height, each 1/8 lap wide, but shorter in metres than the widths at the base.
All crossings are in the same place

## Slide 18
Two consecutive vertical eight (Rule 4.2.15.13)
Crossing at 45° line elevation angle
Highest point at 90° line elevation angle
When flying through the intersection the model flies momentarily horizontal
Loopings circular round shape Manoeuvres bottom/top symmetrical
Manoeuvre right/left symmetrical
Both eights in the same place

## Slide 19
Hourglass (Rule 4.2.15.14)
All turns are tight. Turns flown wide are faults
Width at the bottom and top is slightly more than 1/8 lap (+)
Climb and dive are straight lines along great circle tracks
Crossing at 45° line elevation angle
Upper segment flown along a great circle track offset by 90°
Manoeuvre down/up symmetrical
Manoeuvre right/left symmetrical
Notes: Upper segment flown along a great circle track offset by 90°.

## Slide 20
Two consecutive overhead eight (Rule 4.2.15.15)
Equal sized round loops
Lowest points 45° line angle
Start/end at 90° line angle
Axis of eights 90° to Wingover Path
In the crossing very short along Wingover Path
Manoeuvre left/right symmetrical
Manoeuvre front/rear symmetrical
Both eights at the same place

## Slide 21
Four-leaf clover manoeuvre (Rule 4.2.15.16)
4 circular approx. ¾ loops of the same size.
At the pilot's option and without prior notice to the judges the rule allows the entry into the manoeuvre from the base or, as before, from above at a suitable altitude allowing the correct execution of the first loop.
Upper loops tangential to the 90° wingover path.
"Horizontal" connecting lines along a great circle track inclined upwards by 45°.
Lower loops tangential to the base and vertical axis.
Vertical connecting lines 90° perpendicular to the base.
Manoeuvre left/right symmetrical
Manoeuvre upper/lower symmetrical
Notes: At the pilot's option and without prior notice to the judges, the 2021 edition of the rule allows the competitor to enter the manoeuvre from the base or, as before, from above at a suitable altitude allowing the correct execution of the first loop.
Also new from 1.1.2021, the two "horizontal" connecting sections of the manoeuvre must be flown along a 45° upward tilted great circle track.

## Slide 22
Landing manoeuvre (Rule 4.2.15.17)
The landing manoeuvre begins when the model leaves the base altitude of 1.5 m (+/- 30 cm) in power-off condition.
From the point begin of approach the length of the descent is 1 lap until touchdown.
The descent is steady with a constant angle of approach.
The manoeuvre, and thus the flight, ends when the model comes to a standstill.
Notes: The condition "power-off" is considered to be fulfilled when the engine is switched off and when the propeller blades stand still before touchdown.
Electrically powered models must be held by a helper after coming to a standstill until the drive is secured against unintentional start-up. This is a mandatory rule. Failure to comply will result in a 0 landing score.

## Slide 23
ANNEX 4 B - CLASS F2B AEROBATICS JUDGES’ GUIDE
The regulations in the F2B Judges' Guide in the FAI Sporting Code support the national model flying organisations in their efforts to standardise the training of F2B judges.
3. Judging
Notes: Basic requirements for implementation at national level are:
National organisations are required to translate the regulations and keep them up to date.
In-depth knowledge of the current regulations and the FAI F2B Judges' Guide
Regular training and ongoing further education for judges
Demonstrable proof of the proficiency level of individuals registered as FAI judges.

## Slide 24
Regardless of the person, without consideration of previous performances and uninfluenced by the construction or technology of the model, the only task of the judge is to recognise deviations from the rules and to assess these as faults.
Notes: In competition, the well-trained and experienced judge is an independent expert. He does not allow himself to be influenced by other judges or third parties and avoids corresponding discussions.
In competition, it is not necessary that the scores of one judge agree with those of another. Efforts to "harmonise the scoring" of judges prior to the competition may affect the stability and/or reproducibility of the scoring of individual judges and must be avoided.
It is imperative that the scoring level of a judge remains at the same level throughout the competition.

## Slide 25
Simplified display of frequently observed deviations from the "right path".
4. Typical Errors
Notes: The judge registers each and any deviation from the prescribed flight path.
He weights the extent of the deviation and determines the score from this.
Manoeuvres not, incompletely or in wrong order flown will be scored 0.
A manoeuvre missed by the judge will be scored N.O. (Not observed).

## Slide 26
The hemisphere as seen from the judge
45° Lines Elevation
Base1.5 m
Vertical Centerline
Wingover Path
Overhead Pilot
90° Wingover Line
Notes: The centre of the hemisphere is the location of the pilot; i.e. the highest point of the hemisphere is above the pilot's head.
The spherical distortion from the judge's point of view is clearly visible.
However, since the judge's eye follows the model in flight, this distortion is perceived less distinctly by him.
The following should be noted:
The observance of the lowest and highest points, i.e. the size of the figure.
Are the round loops circular ?
Crossings always at the same place; without overlaps, loops must touch each other.
Is the entry height into the corresponding manoeuvre within 1.2 - 1.8 m ?

## Slide 27
4.2.15.3 Take-off
1.5 m
min. 4.5 m
max. ¼ lap
Rule
Track
Start
End
too high
too short
Uneven climb
too high
less than1 lap from release
after 3 laps
Notes: Too short or too long a take-off run is an error.
Too long or too short a climb is an error.
Uneven climb is a fault.
An altitude of more than 1.8 m or less than 1.2 m during the two rounds of level flight is a fault.
Visible corrections of altitude during the two rounds of level flight are faults.

## Slide 28
4.2.15.4 Reverse wingover
1.5 m
Rule
Track
Start
End
not opposite
too wide
Not Overhead
too high
too high
Notes: The following applies to all cornered manoeuvres:
If one or all turns are flown softly and with a large radius, this is a fault. Depending on the degree of softness and/or the inequality of the radii of individual turns, an appropriate deduction results.
The tighter, more precise and more even the radii of the turns are flown, the higher they are rated in total for the manoeuvre.

## Slide 29
Round loops as seen from the Judge
45° Lines elevation angle
45°
Centerline

## Slide 30
4.2.15.5 Three consecutive inside loops
1.5 m
45 °
D
D
displaced
too wide, too high & displaced
too high
Rule
Track
1 2 3

## Slide 31
4.2.15.6 Two consecutive laps of inverted level flight
Rule
Track
1.5 m +/- 30 cm
Visible correction
above 1.8 m
below 1.2 m
Notes: At the beginning of lap 3 the entry altitude is 1.5 m +/- 30 cm. i.e. between 1.2 and 1.8 m.
During laps 3 and 4 the entry altitude is to be maintained.
Visible corrections of the altitude in laps 3 and 4 are faults.

## Slide 32
4.2.15.7 Three consecutive outside loops
1.5 m
45 °
D
D
displace
too high, too wide & displaced
too high
Rule
Track
1 2 3

## Slide 33
Square as seen from the judge
45° Lines elevation angle
45° l
Symmetrieachse
Notes: The width of the manoeuvre along the base (incl. turns) is 1/8 lap.
The pilot flies the vertical sides 90° perpendicular to the base from his point of view.
At the height of 45° line elevation angle, the upper side is therefore shorter.

## Slide 34
4.2.15.8 Two consecutive inside square loops
1.5 m
45 °
Rule
Track
1 2
too high
too wide
Too narrow, too high & displaced
Notes: The following applies to all cornered manoeuvres:
If one or all turns are flown softly and with a large radius, this is a fault. Depending on the degree of softness and/or the inequality of the radii of individual turns, an appropriate deduction results for the manoeuvre (but not for individual turns).
The tighter, more precise and more even the radii of the turns are flown, the higher they are rated in total for the manoeuvre.

## Slide 35
4.2.15.9 Two consecutive outside square loops
1.5 m
45 °
too high
too wide
displaced
Rule
Track
1 2
too high
too wide
Notes: The following applies to all cornered manoeuvres:
If one or all turns are flown softly and with a large radius, this is a fault. Depending on the degree of softness and/or the inequality of the radii of individual turns, an appropriate deduction results .
The tighter, more precise and more even the radii of the turns are flown, the higher they are rated in total for the manoeuvre.

## Slide 36
Triangular Looping as seen from the judge
45° Lines elevation angle
45°
Symmetrieachse

## Slide 37
4.2.15.10 Two consecutive inside triangular loops
1.5 m
45 °
Rule
Track
1 2
too high
too wide
Asymmetric
& too wide
too flat
Notes: The following applies to all cornered manoeuvres:
If one or all turns are flown softly and with a large radius, this is a fault. Depending on the degree of softness and/or the inequality of the radii of individual turns, an appropriate deduction results .
The tighter, more precise and more even the radii of the turns are flown, the higher they are rated in total for the manoeuvre.
The bottom side is slightly wider than 1/8 lap.
The highest point is at 45° line elevation angle.

## Slide 38
Horizontal Eight
as seen from the judge
45° Lines elevation angle
45°
Crossing line

## Slide 39
4.2.15.11 Two consecutive horizontal eight
1.5m
D
45°
D
Rule
Track
1 2
Above 45O
Displaced crossing
off centerline
too low
Notes: The position of the crossing axis is determined when flying through the "start" position for the first time.
Corrections to the size and position of the loops lead to deviations from the circular shape and are errors.
Loops that are too far apart lead to crossings where the model never flies vertically for a short time.
Overlapping loops make it impossible to keep the crossing axis.

## Slide 40
Square Eight
as seen from the judge
45°
45°
Crossing line

## Slide 41
4.2.15.12 Two consecutive horizontal square eights
1.5 m
45o
Rule
Track
1 2
slanted
slanted
too large
too soft
Above 45o
off center
too low
displaced
below 45o
too soft
Notes: The position of the crossing line is determined when the model flies vertically upwards after passing the "start" position for the first time.
The width of the two squares at the base (incl. turns) is 1/8 of a lap.
The pilot flies the vertical sides on the crossing line and the outer sides perpendicular to the base.
Therefore, at the 45° line elevation angle, the upper sides are shorter.
If one or all turns are flown softly and with a large radius, this is a mistake. Depending on the degree of softness and/or the inequality of the radii of individual turns, an appropriate deduction results.
The tighter, more precise and more even the turns are flown, the higher they are rated in total for the manoeuvre.
All crossings are flown on the same initial crossing line.

## Slide 42
Vertical Eight as seen from the Judge
45°
45°
Symmetry axis

## Slide 43
D
4.2.15.13 Two consecutive vertical eight
1.5 m
45°
90°
Rule
Track
1 2
behind overhead
asymmetric
too high
off center
too low
Notes: Start and end at the crossing point
Both loops circularly round and of equal size
The crossing point is at 45° line angle
At the crossing point the model flies momentarily horizontal
The highest point is at 90° line angle
The manoeuvre is symmetrical right/left

## Slide 44
Hourglass as seen from the judge
45°
45°
Symmetry axis
90° wingover path

## Slide 45
4.2.15.14 Hourglass
1.5 m
45°
Regel
Flugweg
90° (Wingover path)
twisted
behind overhead
too flat
too soft
too wide
off center
Notes: The width of the lower and upper sides, including the turns, is slightly more than 1/8 lap.
The upper side is flown along a wingover path (great circle) oriented 90° to the manoeuvre.
If one or all turns are flown softly and with a large radius, this is an error. Depending on the degree of softness and/or the inequality of the radii of individual turns, an appropriate deduction results.
The tighter, more precise and more even the turns are flown, the higher they are rated.
The crossing point is on the vertical axis of symmetry and at 45° line angle.
The straight climb or descent segments are flown along a great circle track.
The manoeuvre is right/left symmetrical

## Slide 46
Overhead Eight as seen from the judge
45°
45°
Centerline
90° Wingover Path

## Slide 47
4.2.15.15 Two consecutive overhead eight
Pilots View Diagram
Rule
Track
1 2
45° Altitude
90o Wingover Line
Wingover Linie
Below 45o
above45o
above 45o
displaced from center
Not on 90o Wingover Line
displaced from center
off center
Notes: The front/rear symmetry axis is on a wingover line positioned 90° to the manoeuvre.
The right/left axis of symmetry is on the wingover line between the pilot and the judge.
Intersections and highest point above the pilot's head.
Lowest points at 45° line angle.

## Slide 48
4-Leaf Clover as seen by the judge
45° Line angle
Centerline
90° Wingover Path
Line angle approx. 42°

## Slide 49
4.2.15.16 Four-leaf clover manoeuvre
1.5 m
max. 45°
Rule
Track
90° Wingover Linie
approx. 42°
displaced
too high
too low
displaced
too low
Connecting lines not along great circle
Notes: New from 1.1.2021:
The entry may be performed, optionally and without prior notice from the pilot, with a vertical climb from the base or from above at an altitude of approximately 42° line elevation angle.
4 circular approx. ¾ loops of the same size.
Upper loops tangential to the 90° wingover line.
"Horizontal" connecting lines are flown along a great circle track inclined upwards by 45°, i.e. slightly curved upwards.
Lower loops tangential to the base and to the vertical axis.
Vertical connecting lines 90° perpendicular to the base.
Left/right halves symmetrical.
Upper/lower halves symmetrical.

## Slide 50
4.2.15.17 Landing Manoeuvre
1.5 m
Rule
Track
too low
too high
stop
less than 1 lap
Touchdown after 1 lap descent
Begin of descent
Notes: The landing begins when the model leaves the base height of 1.5 m (+/- 30 cm) in power-off condition.
The condition "power-off" is considered to be fulfilled when the engine is switched off and when the propeller stops before touchdown.
From the beginning of the descent, the length of the landing approach is 1 lap until touchdown.
The landing approach is steady i.e. with a constant approach angle.
The manoeuvre, and thus the flight, ends when the model comes to a standstill.
Electrically powered models must be held by a helper after coming to a standstill until the drive is secured against unintentional start-up. Failure to do so will result in a score of 0 for the landing.

## Slide 51
The weighting of detected errors is the sole responsibility of the judge.
He shall make use of the whole range of available scores.
It is of crucial importance that the determination of deductions for specific errors always remains the same throughout the competition.
5. Error Weighting and Scoring
It is not the purpose of judging at a competition to have all judges award the same marks for a manoeuvre.
The aim is for each judge to score the observed faults consistently throughout the competition according to his or her own standard.

## Slide 52
Notes: The video contained in this presentation is not authorised for commercial use or publication.

## Slide 53
Notes: Click on image to run video:
Stop after each manoeuvre.
Find, discuss and weigh mistakes together.
Repeat with only short stops and determine the marks.

## Slide 54
Questions and suggestions on how to improve
Notes: Thank you for your patience and great commitment.
Just as for the pilots, it is equally important for the judges to expand their basic knowledge through constant training and participation in further training and competitions and thus to maintain their proficiency at a high level.

## Slide 55
Thank you very much for your participation. You are making a sustainable and valuable contribution to our common cause.
Made by Peter Germann, Switzerland
Supported by Keith Renecle, South Africa
Toni Borer and Louis Winkler, Switzerland.
Video post-processing by Alberto Solera, Spain.